# Bubble Wraps

Source: BUILDER Magazine
Publication date: September 1, 2005

By Charles Wardell

Q: What are the pros and cons of open-cell and closed-cell foam insulations? And where are the best places to use each?

A: BLOWN-IN-PLACE POLYURETHANE foams are a blend of isocyanates and urethane resins that are mixed in a spray nozzle, then blown into a wall or ceiling cavity. A blowing agent makes the foam expand and fill the space.

Open-cell and closed-cell foams use different blowing agents. They also differ in hardness, insulating value, vapor permeability, and cost.

AIR AND GAS

The most familiar brands of open-cell foams are Icynene and Demilec. These use water as a blowing agent and insulate by trapping air in microscopic cavities that are connected to one another like the voids in a sponge.

Closed-cell foams are blown with gas, which also acts as the insulator. As the foam expands, it traps the gas in a matrix of tiny spheres, each about the diameter of a human hair—a kind of microscopic, three-dimensional bubble wrap. Unlike the air in an open-cell product, very little of the gas trapped in these bubbles leaks out. Insulation manufacturers buy the blowing agent, package it with the urethane mixture, then sell the system to insulation contractors.

Until recently, the blowing agents used in closed-cell foams included chlorine-based chemicals, which deplete the earth's ozone layer, but manufacturers are switching to more environmentally benign products. For instance, Honeywell's new Enovate gas (HFC-245 fa), which is used by some of the biggest insulation manufacturers, is a hydro-fluorocarbon gas that includes non-ozone-depleting fluorine.

COMPOSITION AND DENSITY

Open- and closed-cell foams have different compositions and densities. Open-cell foams are soft and pliable, with densities of ½ to ¾ pounds per cubic foot. “They're like a cushion, or the packaging material molded inside a plastic bag to fit a fragile object being shipped,” says Steve Riddle, vice president of sales with North Carolina Foam Industries (www.ncfi.com), a nationwide installer of open- and closed-cell foams.

Closed-cell foam, by contrast, has a density of around 2 pounds per cubic foot; in fact, it's stiff enough to walk on without crushing it. Says Riddle: “The bubbles in a closed-cell foam are strong enough to take a lot of pressure, like the inflated tires that hold up an automobile.”

Riddle's installers find that closed-cell foam, because it's so rigid, will actually stiffen wall assemblies by helping lock a home's framing members together, making it the insulation to use in high-wind areas. This field experience has been confirmed by laboratory research.

“There has been a lot of testing done on the racking strength provided by different types of spray foams,” says Tom Kenny, of the NAHB's Research Center, in Upper Marlboro, Maryland. “And the strength provided by closed-cell foams can be substantial.”

However, Kenny points out that this strength isn't acknowledged by building codes. In other words, while closed-cell foam can help stiffen a structure in a high-wind zone, you can't reduce the structural bracing as a trade-off.

INSULATING VALUE

The insulating value of any foam depends on the gas trapped inside of it. Because a gas like Enovate is a better insulator than air, closed-cell foams give you more R-value per inch. Some open-cell manufacturers like to differentiate their product by pointing out that it has a stable R-value, while gas leaking from the closed-cell product degrades its effectiveness over time. Riddle says this is misleading. Closed-cell foams do lose some gas soon after installation, but they stabilize over time, and their long-term R-value is still impressive. In fact, his company advertises its closed-cell foam's long-term R-value of 6.8 per inch, which is nearly twice that of open-cell's R-value of 3.5 per inch.

AIR AND VAPOR SEALING

Both foam types resist the passage of water vapor better than fiberglass or cellulose, but closed-cell foams do it best. In fact, some closed-cell foams have a perm rating of less than 1.0, the standard perm rating for a vapor retarder.

OPEN OR SHUT CASE

Choosing the right cell foam involves more than just comparing prices.

|  | Open-cell | Closed-cell |
| --- | --- | --- |
| Blowing Agent | Water | HFC-245 fa |
| Insulator | Air | HFC-245 fa |
| Long-term insulation value | R-3.5 per inch | R-6.8 per inch |
| How it insulates | Air is trapped in an open matrix | Gas is trapped in sealed spheres |
| Composition | Soft like a sponge Low Compression Strength | Hardness depends on density High Compression strength |
| Structural Strength | None | Adds racking strength to walls and ceilings |
| Air Barrier | Yes | Yes |
| Permeability | 10 (May require a vapor retarder) | 1.0 (Can be used as a water barrier) |
| Best Use | Where cost is a consideration In warm climates where moisture won’t condense in the wall | Wherever you need high R-value or where moisture contact is possible. Crawl spaces, attics, and other places where vapor sealing is critical |

Under normal circumstances this may not mean much: Condensation in walls and ceilings is usually caused by leakage of moist air, not differences in vapor pressure, and even low-density foams do a good job of blocking air movement. However, Riddle recommends using closed-cell foam where outside water is a concern: on the coast, in flood-prone regions, in crawl spaces, and in attics. (His company even uses it as a flat roof covering. It sprays it on the roof surface, then covers it with gravel.) It's also a good choice where you need to get a lot of insulating value into a small space.

THE BOTTOM LINE

One disadvantage of closed-cell foam is it costs more per inch than open-cell, since it's denser and requires more material. Cost per R-value can vary in different parts of the country, so you'll have to check with your installer.

The choice of foam should be based on the requirements for strength and vapor control, available space, and so on. “We select a foam system depending on the particular requirements of our clients' projects,” says Riddle. The table on this page includes some suggested uses.

Charles Wardell is a freelance writer based in Vineyard Haven, Mass.

SOURCE: NORTH CAROLINA FOAM INDUSTRIES